## Slide 1: The Rolling Mean and Standard Deviation Dataset charts allow for identification of abnormalities –Horse Power, Pump Torque, and Pump Speed measures all spike dramatically just prior to pump failure
Chart: Rolling Mean - All Variables
Chart: Rolling Standard Deviation - All Variables
Notes: From the Rolling Mean chart, it's clear to see that horse power and pump torque spike just before the pump failure, then sharply decrease along with all of the other variables. We can also see there's a large increase of all of the variable's rolling standard deviations during the pump failure - this is probably due to the larger variance in the data (unusually large increase / decrease in values) during the failure.

## Slide 2: A clear difference in the data’s spread during normal pump operation vs. failure can also be seen below - Pump Torque, Pump Efficiency, and Pump Speed exhibit the most variance during failure

## Slide 3: Correlation analyses across datasets yield more interesting insights… All variables (except HP) are negatively correlated with failure in the Rolling Mean Data, only Flow Meters 1 & 2 and Pump Efficiency are negatively correlated with failure in the Raw Data Set, while HP has strong positive correlation with failure in all data sets
Chart: Correlation Strength Associated with Pump Failure (Raw Data Set)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.42184 | 0.26001 | 0.23318 | 0.20801 | -0.10249 | -0.10268 | -0.11211
Chart: Correlation Strength Associated with Pump Failure (Rolling Mean Data Set)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.21803 | -0.18417 | -0.21603 | -0.30265 | -0.69244 | -0.69503 | -0.69773
Chart: Correlation Strength Associated with Pump Failure (Rolling St Dev Data Set)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
 | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726
Notes: Raw Data Correlation Notes: There is a negative relationship between Pump Failure and Volumetric Flow Meter 1, Volumetric Flow Meter 2, and Pump Efficiency. There's a positive relationship between Pump Failure and Pump Speed, Pump Torque, Ambient Temp, and Horse Power. Horse Power has the strongest relationship (positive) with Pump Failure.
Rolling Mean Correlation Notes: There is a strong negative relationship between the rolling mean of Pump Failure and Volumetric Flow Meter 1, Volumetric Flow Meter 2, and Pump Efficiency. The only positive relationship with Pump Failure among the independent variables is Horse Power, however the relationship is not that strong.
Rolling St Dev Correlation Notes: These correlation coefficients show the strongest relationships between Pump Failure and the independent variables. All of the rolling standard deviations (variance) have a fairly strong positive relationship with Pump Failure. Horse Power's rolling standard deviation has the strongest positive relationship with the rolling standard deviation of Pump Failure. When looking at analyzing time series data and events of interest, we should pay particularly strong attention towards variables which exhibit the largest degree of statistical variance.

## Slide 4: Lastly, analysis of the model’s fit reveals that a linear model is a good fit for the data, with Horse Power, Pump Efficiency, and Volumetric Flow Meter 2 having the largest absolute impact on pump failures (greatest regression coefficients)
Chart: Regression Coefficient Ranking
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
 | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136
As Horse Power and Pump Efficiency rise, so does the predicted chance of pump failure
As Volumetric Flow Meter 2 increases, the predicted chance of pump failure actually drops
The model’s R-Sq value of 0.778 indicates 77.8% of variability in the dependent variable can be explained by the model
The model is also statistically significant, as all of the ind. variables’ p-values are below the significance level of 0.05
The model can be used to help predict future outcomes with confidence

## Slide 5: With the model, a proactive alarm has been created, which accurately identifies pump failures before they occur. Horse Power (HP) and Pump Efficiency (PE) are key variables to monitor, with deviations of 15 HP and >3% PE being their signal thresholds
Chart: Pump Failure Alarm Chart
The regressive prediction doesn’t exceed ~0.2, unless a failure is imminent, serving as a good alert for when preventative action should be taken